## Slide 1
KVN
Advances in Source/Frequency Phase Referencing with KVN
Astrometric comparison of sites of maser emission in R Leo Minoris.
Richard Dodson:
Brain Pool Fellow@KASI

## Slide 2
KVN
KVN observations of R Leo Min.
Largely covered in paper on R Leo Minoris, where we observed R LMi in H2O and SiO v=1,2 J=1-0 with 4C39.25 as phase reference calibrator. Dodson et al, AJ, 2014, in press
Summary:
SiO and H2O masers around AGB stars
What Astrometry of these will tell us
Difficulties of Astrometry at high frequencies
Review the Source Frequency Phase Ref. Method
Stress differences for SFPR between line and cont.
R LMi astrometric images in H2O and SiO

## Slide 3
KVN
SiO masers around AGB Stars
SiO masers have high excitation energy, so form close to star
Pumping mechanism a matter of vigorous debate.
Radiative (Bujarrabal 1994).
SiO masers are pumped by 8 µm stellar radiation.
Requires: a thin shell emitting region and/or radialstrong accelerations
Explains: SiO rings (tangential amplif.)
Linear Pol
Correlation of SiO and IR fluxes

## Slide 4
KVN
SiO masers around AGB Stars
SiO masers have high excitation energy, so form close to star
Pumping mechanism a matter of vigorous debate.
Collisional (Humphreys et al. 2002). SiOmasers are pumped by collisions with H2, and shocksinduced by the stellar pulsation.
Explains: SiO rings (tangential amplif.)
Linear Pol
Requires: very high (100km/s) propagation speeds
to achieve the SiO/Optical Phases

## Slide 5
KVN
A rant about astrometric comparisons
If you compare two images without astrometric registration you are speculating ...
You have not proved anything
You might be right -- but equally you might be wrong

## Slide 6
KVN
A rant about astrometric comparisons
If you compare two images without astrometric registration you are speculating ...
You have not proved anything
So .. how do we do it correctly?
Phase Referencing
You might be right -- but equally you might be wrong
(Also true for cont. images)

## Slide 7: Phase Referencing
KVN
The default calibration in VLBI is Self Calibration
Calibrate the data using the large N inputs
to solve for the small M variables.
Requires: Strong Signals
Delivers: High dynamic range image, but position information lost
The alternative is Phase Referencing
Calibrate the data using the (selfcalibration) solutions from a nearby known source.
Ideal for: Weak sources and provides Astrometry
Conditions:
* Nearby strong point source
* 1.6GHz < ν < 43GHz
IONO TROPO
But Phase referencing at 43GHz is very hard
Notes: Quick Intro to PR. If needed
PR has provided a huge increase in the useability of VLBI

## Slide 8: Alternative Tropospheric Calibration for mm-VLBI
KVN
Observe at lower band (e.g. 21.5 GHz)
Apply to higher band (e.g. 43 GHz)
Conventional Phase referencing to a calibrator source
(requirements difficult to meet)
Multi-frequency: phase ref. to a lower frequency
fast
Same source
43 GHz
43
fast
Different
source
Notes: But mm-VLBI phase referencing is really hard.
You have to switch very fast (and so) your calibrator needs to be very close. And they are not so many which are bright enough.
To my knowledge only 86GHz PR is P&R 2000 on the 1308+32 pair.
But for any source there is a source at 0 deg sep. So why not use the low freq to calibrate the high freq and switch rapidly between the freq?

## Slide 9: Basics of new method: SOURCE/FREQ. phase referencing
KVN
φΑ = φ A,GEO + φA,TRO + φA,ION + φA,STR + 2πnA
φA,TRO - R * φA,TRO = 0, Atmosphere errors cancel
φA,ION - R * φA,ION = (R-1/R) ∗ φA,ION
φΑ−R∗φΑ = (φΑ,STR + 2πν/c (D . θA,shift)) + ΙΟΝ + ΙΝST
X
R = ν / ν
fast
slow
slow
slow
slow
…
φA,XYZ - R * φA,XYZ = 0, Antenna errors cancel
Frequency Phase Transfer
High:
Low:
High:
X
φΑ = φ A,GEO + φA,TRO + φA,ION + φA,STR + 2πnA
R*φΑ = R* (φ A,GEO + φA,TRO + φA,ION + φA,STR + 2πnA)
Target
Notes: Step 1 Freq Phase Transfer:
Phase in VLBI visibilities (high freq green) are made of multiple contributions:
Geometric, Tropospheric, Ionospheric, Instrumental, Structual + N2pi:
Some of these are fast some are slow:
The low freq (red) situation is the same: If we scale the low by the ratio: non-dispersive go to zero. Ionosp made LARGER (but start small): So phase residuals are Structure, Core shift and slow changing Iono and Inst.

## Slide 10: Basics of new method: SOURCE/FREQ. phase referencing
KVN
Introduce a Second Source B
φΒ−R∗φΒ = 2πν/c (D . θB,shift) + ION + INST
Source/freq. referenced Visibility phase:
φA,STR + 2πν/c ∗ D (θA,shift - θB,shift)
Same as for A
KVN
Notes: Rather than SelfCalibrating. We can introduce a second source. With same proceedure we end up with residuals with Core-shift (Structure) and Iono and Inst.
Alternating between A and B allows us to separate out structure and combined core-shift.

## Slide 11: Important points
KVN
“Perfect” Tropospheric calibration
→ increased coherence time (for weak sources)
Extends Phase Referencing to the Highest Frequencies
Calibrator can be much further away
Direct Astrometric measurement, even
at the highest frequencies > 43 GHz
BUT assumed integer ratio between frequencies
Frequency agility crucial: VLBA (switching);
Much better to sim. observe than switch
as for KVN (& potentially others)
Notes: Summary points
Long Coherence Times = Sensitive obs.
PR at > 43GHz
Robust

## Slide 12: SFPR for Masers lines:
KVN
Maser lines rarely have integer freq. ratios
(v=x, J=1-0 & J=2-1, etc do
but not H2O to SiO)
R*φΑ = R* (φ A,GEO + φA,TRO + φA,ION + φA,STR + 2πnA)
If R not integer then R*2πnA introduces phase jumps
Makes the astrometric calibration impossible.
(but phase stabilisation still works)
Unless nA is carefully tracked

## Slide 13: SFPR for Masers lines:
Line SFPR
Geodesy
KVN
We have developed an approach which will
keep ΔnA zero
One (just) has to ensure that there are no phase ambiguities, that is the:
Antenna positions are good
Source positions are good
Normal
Calibration
Normal
phase referencing
Normal
SFPR
line
SFPR
*1.9
FRING
Una Selva Obscura
We can do it
Don’t Panic
Notes: Phase Referenced images from the KVN, referenced between 22 and 43 GHz (both SiO transitions)
redone with new (<5cm) positions

## Slide 14: Astrometric comparison of maser emission in R Leo Minoris.
KVN
Transfer H20 maser
corrections to SiO data with scaling factors
Hipparcos Position
(with 1𝜎 PM errors)
VLBI Position
(with 1𝜎 PR errors)
SiO maser phase referenced to H2O maser.
Errors between:
SiO v=1 & 2 ~35μas
SiO & H2O ~ 2mas
Centre of SiO ~ 5mas
v=1 & 2: 1mas
Sep. H2O/SiO: 70mas
Ring Size: 20mas
Notes: Resuits from AJ paper

## Slide 15: Conclusions:
KVN
the Source Frequency Phase Ref. Method for line
sources is now understood.
Successful astrometric alignment of images
of H2O and v=1 & 2 SiO masers in R LMi with KVN
Absolute astrometric alignment to improve R LMi
proper motion measurement
Pumping model predictions for SiO in KVN bands can
be checked.
Astrometrical aligned images between H2O and SiO
H2O and CH3OH can be formed.

## Slide 16: Multi-frequency Phase Referencing (MFPR):
KVN
KVN has capability to observe at 4 frequencies
Can we solve for all the atmospheric contributions?
  3 unknowns, 4 frequencies – should be possible
VLBA also has wide frequency range
  Can we fast-frequency switch in mm-band & add slow-frequency switch in cm-band to do this?
  Measure static ionospheric contributions; new
    version of geodetic blocks?

## Slide 17: Can we go further? Multi-Freq phase referencing
KVN
Freq 1 (22GHz) φΑ = φ A,GEO + φA,TRO + φA,ION + φA,STR + 2πnA
Freq 2 (43GHz) φΑ = φ A,GEO + φA,TRO + φA,ION + φA,STR + 2πnA
Freq 4 (129GHz) φΑ = φ A,GEO + φA,TRO + φA,ION + φA,STR + 2πnA
FPT12 =(2-1/2)*φA,ION
FPT13 =(4-1/4)*φA,ION
Freq 3 (86GHz) φΑ = φ A,GEO + φA,TRO + φA,ION + φA,STR + 2πnA
FPT23 =(2-1/2)*(φA,ION /2)
FPT24 =(3-1/3) *(φA,ION /2)
FPT23 =(2-1/2)*φA,ION
FPT24 =(3-1/3) *φA,ION
Assuming Inst. Cal done
& no structure phase

## Slide 18: Can we go further? Multi-Freq phase referencing
KVN
Freq 1 (22GHz) φΑ = φ A,GEO + φA,TRO + φA,ION + φA,STR + 2πnA
Freq 2 (43GHz) φΑ = φ A,GEO + φA,TRO + φA,ION + φA,STR + 2πnA
Freq 4 (129GHz) φΑ = φ A,GEO + φA,TRO + φA,ION + φA,STR + 2πnA
FPT12 =(2-1/2)*φA,ION
FPT13 =(4-1/4)*φA,ION
Freq 3 (86GHz) φΑ = φ A,GEO + φA,TRO + φA,ION + φA,STR + 2πnA
FPT23 =(2-1/2)*(φA,ION /2)
FPT24 =(3-1/3) *(φA,ION /2)
Expected Ratios:
Ref Target | FPT12 | FPT13 | FPT23 | FPT24
FPT13 | 2.5 | 1 | - | -
FPT23 | 0.5 | 0.8 | 1 | -
FPT24 | 0.9 | 0.7 | 1.8 | 1

## Slide 19: Can we go further? Multi-Freq phase referencing
KVN

## Slide 20: Can we go further? Multi-Freq phase referencing
KVN
Expected Ratios:
Ref Target | FPT12 | FPT13 | FPT23 | FPT24
FPT13 | 2.5 | 1 | - | -
FPT23 | 0.5 | 0.8 | 1 | -
FPT24 | 0.9 | 0.7 | 1.8 | 1
Found Ratios:
Ref Target | FPT12 | FPT13 | FPT23 | FPT24
FPT13 | 3-3.3 | 1 | - | -
FPT23 | 2-1 | ~1-2 | 1 | -
FPT24 | ? | ~2-3 | 1.4-3.8 | 1

## Slide 21: Non-Conclusions:
KVN
the Multi-Frequency Phase Ref. Method needs more work before it is understood.
Looks like that these are not ionospheric residuals
  In which case our approach will not succeed.
Could these be instrumental residuals?
  If so perhaps these can be measured independently and removed, revealing the expected behaviour?