## Slide 1
Aperture Array Design & Construction Consortium
Low Frequency Aperture Array (LFAA)
Signal Processing and Commissioning Software
University of Oxford/Malta
Prepared by: Kristian Zarb Adami and Alessio Magro

## Slide 2: The LFAA system
Monitoring and Control System

## Slide 3: TPM firmware

## Slide 4: AAVS0.5 DSP Firmware Architecture
JESD20B IF
CHANNELIZER
BEAMFORMER
CSP SPEAD
FORMATTER
4x10G ETHERNET
AXI4 LITE BUS
C2C MM
AXI4LITE
Bridge
LMC SPEAD
FORMATTER
AXI4 STREAM C2C STREAM Bridge
ADC
CPLD
(c&c)
QSFP
CPLD
(LMC data)
POWER
INTEGRATOR
POWER
INTEGRATOR
AXI4 LITE
AXI STREAM

## Slide 5: AAVS0.5 DSP Firmware Modules
Data to LMC server through 1G Ethernet
  Raw ADC data, 64 Kbytes snapshot from 1 antenna
  Synchronized Raw ADC data, 64 Kbytes snapshot from 16 antenna
  Continuous channel mode, 1 frequency channel of channelized data from 16 antenna
  Burst channel mode, variable number of samples from 1 frequency channel rotating through all channels, 16 antenna
  Beamformed data, 64 Kbytes snapshot
  Integrated channel data, power spectrum, programmable integration time
  Integrated beam data, power spectrum, programmable integration time
Data through 40G Ethernet
  Beamformed data, 1 beam, ~7.5 Gbit/s

## Slide 6: AAVS0.5 DSP Firmware Modules
JESD204B
  16 serial lines per FPGA, 8 Gbit/s per line, ADCs operate at 800 MHz 8 bits per sample
  Synchronized ADCs operation using JESD204B Subclass-1 between FPGAs in the TPM has been tested
  Synchronization between different TPMs to be verified
Channelizer (undergoing field testing)
  Provided by INAF
  512 frequency channels
  32/27 oversampling factor
Beamformer (undergoing field testing)
  Provided by University of Malta
  Single beam
  Full BW, 400 MHz
  Run-time configurable weights using shadow memory

## Slide 7: AAVS0.5 DSP Firmware Modules
4x10G Ethernet / SPEAD formatters (LMC and CSP)
  Provided by RAL
  Tested in the lab, undergoing field testing
AXI4 LITE Infrastructure
  XML2VHDL Python script used for generating VHDL code of AXI4 Lite slave interfaces from XML registers description
  Adopted throughout the design
  Tested on field
AXI4 STREAM Infrastructure
  Streaming library including MUX, DEMUX, PIPELINE, FIFO,…
  Tested on field

## Slide 8: AAVS1 DSP Firmware Ongoing Development
Tile Beamformer supporting multi-beam
Station beamforming is performed by an Ethernet connected TPMs chain
Each TPM receives beamformed data from the previous TPM and combines the received data with the produced tile beam. Then it transmits the combined beam to the next TPM in the chain
DDR3 and FPGA2FPGA High-speed link are needed to address this architecture

## Slide 9: Firmware Status
Requirement | Status
JES-D | I
Channelizer | I
Beamformer | P
CPLD | I
4 x 10Gb-E | I
1 x 40Gb-E | D
FPGA-FPGA | P
DRAM | P
ADC Synch | I
Board Synch | P
Legend:
D In Design
P In Progress
I Implemented
N Not started

## Slide 10: AAVS1 Rack Status
PDU/PSU delivered
TPM(s) ordered
Clock distribution (delivered)
40-GbE switch delivered
1-GbE switch delivered
Fans (on order)
PSU
1Gb SWITCH
CABLE TRAY
OPTICAL FIBRE DIST.
TPM
CABLE TRAY
CLOCK DIST.
40Gb SWITCH
1Gb SWITCH
CABLE TRAY
OPTICAL FIBRE DIST.
TPM
CABLE TRAY
CLOCK DIST.

## Slide 11: LFAA Software
O(104) hardware devices to monitor and control
O(102) GB/s processed for calibration
Raw antenna data is trickled through the same network to an HPC system
A software architecture using large scale control systems and cloud-based technologies is being developed in collaboration with industry

## Slide 12: AAVS1 Overall Architecture

## Slide 13: Software Architecture

## Slide 14: AAVS0.5
TPM Control
  Download firmware
  Initialize and control all devices on TPM
  Interact with loaded firmware
Data Acquisition
  Receive LMC data from TPM (7 types)
  Receive station beams (buffers)
  Save to HDF5 files
  Online plotting functionality for testing
Pointing (under test)
  Point to arbitrary ALT/AZ and RA/DEC

## Slide 15: How many cables does it take…

## Slide 16: Towards AAVS0.75
AAVS0.75 will include 4 TPMs, and this is where things start getting interesting:
  Synchronization across TPMs
  Data flow between Tiles
  Synchronized software-level operations across Tiles (eg: application of pointing coefficients)
New devices introduced to the system:
  40GbE switch
  Clock distribution unit
  PDU/PSU

## Slide 17: AAVS0.75
TANGO deployed and tested (connected to a working system) in AAVS0.75
TANGO must be capable of synchronizing operations across Tiles when required (through access layer)
Clock synchronization procedure
New device drivers: switch, server, PDU, PSU
DAQ has to be updated to handle streams from multiple tiles (especially for calibration)
Correlator for calibration
Rolled integration with TM Emulator

## Slide 18: Towards AAVS1
Requirement | Status
TPM driver | I
Switch driver | I
PDU/PSU driver | N
Server driver | P
Rack driver | N
Control System Bus | I
Logging | P
Alarms | P
Events | P
Archiving | N
Requirement | Status
Job System | P
Telescope Model | P
Sky Model | D
Observation modes | P
Cluster Management | N
API and LMC driver | P
DAQ | P
Correlation | D
Pointing | I
Calibration | D
D In Design
P In Progress
I Implemented
N Not started

## Slide 19: Towards AAVS1
TPM driver periodically updated when new firmware functionality is available
Job system for initial AAVS1 deployment will simply use services (Aurora to be investigated after initial deployment)
Likewise, cluster management will initially be very simple
LMC driver acts as the top-level LMC manager, whilst the API is a wrapper to communicate with it
Significant effort will be required to integrate all requirements into a working, stable system (lots of testing)

## Slide 20: TM Emulator
A web-based front end for telescope operators and observers, emulating the role of Telescope Manager
Allows operators to monitor and control telescope hardware through appropriate views of the telescope setup
Allows observers to configure and monitor observations
The emulator is under development (with industry) and an end-to-end test from emulator to TPM has been successfully performed
Python, Django, Nginx, bootstrap, MySQL

## Slide 21: TM Emulator

## Slide 22: TM Emulator

## Slide 23: TM Emulator
Insert screenshot

## Slide 24: TM Emulator
Insert screenshot

## Slide 25: TM Emulator
Insert screenshot

## Slide 26: TM Emulator
Insert screenshot

## Slide 27: Interface with MWA
MWA will have two interfaces with AAVS1:
  AAVS-MWA interface for beamformed data (data path)
  MWA-AAVS control interface (control path)
MWA must be capable to taking over control of AAVS1, that this, create and launch observations
This will happen through the same REST interface which the Telescope Emulator uses
Three primitives: define, start and stop observation
No async control feedback is required

## Slide 28: AAVS1+
Once the system for AAVS1 is deployed and substantially tested, additional low-priority requirements may be implemented:
  Cluster management with Mesos (and maybe DC/OS)
  Job management with Aurora
  Distributed File system with GlusterFS
  Design to handle multiple concurrent observations
  Design to handle more than one beam per station
  Re-direction of station beams to LMC cluster for science pipelines

## Slide 29: SKA LMC Harmonization ANT TEAM
One member on the LMC Harmonization ANT Team
Writing SKA Control System Guidelines document (replacing LIG, TIG, LSR)
Managing sub-teams for:
  Element Alarms and Central Alarms Handling
  Element Archiving and Central Archiving
  Time stamped commands
Participating in sub-teams for:
  Element configuration and sequencing
  Multi-parameter setting and LMC role in configuration
Development of SKA base-devices